## Slide 1: Practical lesson #3
Exercises on Ore minerals, properties of minerals

## Slide 2: The Grade of an Ore
The grade of an ore is the fraction by mass of the valuable material it contains. If:
The mass of the ore = M The mass of valuable material contained = m Then the grade (in %) = m/M * 100
Sometimes, the ore is described in terms of its ore mineral content.
It can then be converted to metals grade using the appropriate relative atomic masses.
For example, a rock containing 1% of chalcopyrite (CuFeS2) would have a grade of:
1 x 63.5 (63.5+ 56 +2x32)
= 0.34% Cu
Where the atomic masses of Cu, Fe and S are 63.5, 56 and 32 respectively.
The grade above which a given deposit is not economic to mine is known as the cut-off grade. Ores well above this value are termed high-grade; those close to this value are termed low-grade.
The multiplication factor needed to reach the cut-off grade from the average crustal abundance is known as the concentration factor. As shown below, this can vary greatly from metal to metal. In general, the greater the concentration factor, the more expensive the metal.

## Slide 3
 | Ave. crust | Ave. cut-off (%) | (%)Conc. factor
Aluminium (AI) | 8 | 30 | 3.75
Iron (Fe) | 5 | 25 | 5
Copper (Cu) | 0.005 | 0.5 | 100
Tin (Sn) | 0.0002 | 0.2 | 1000
Gold (Au) | 0.0000004 | 0.0008 | 500
Mercury (Hg) | 0.000008 | 0.2 | 25000
The multiplication factor needed to reach the cut-off grade from the average crustal abundance is known as the concentration factor. As shown below, this can vary greatly from metal to metal. In general, the greater the concentration factor, the more expensive the metal.

## Slide 4: Exercises
Calculate the Grade of copper-bearing ore, if ore deposit contains 3.2 % of chalcopyrite (CuFeS2)
Calculate the Grade of lead-bearing ore, if ore deposit contains 2.3 % of galena.
Calculate the Grade of iron- bearing ore, if ore deposit contains 3.1 % of Fe203.
Calculate the Grade of iron- bearing ore, if ore deposit contains 4.6 % of Fe304.
Calculate the Grade of zink-bearing ore, if ore deposit contains 5.1 % of sphalerite.

## Slide 5: The required data for calculating the potential mineral deposit value is explained in the table below.
Required Data | Description/ | Example
Average Grade Среднее содержание | The concentration of a mineral in the ore body (i.e. % or g/t) Концентрация минерала в рудном теле | 2% copper and 1.5 gram per tonne gold
Strike Length длина по простиранию | The length in which the mineralization is found in the ore body (horizontally) Длина, на которой минерализация находится в рудном теле (по горизонтали) | 500 meters
Depth глубина | The depth in which the mineralization is found in the ore body (vertically) Глубина залегания минерализации в рудном теле (по вертикали) | 200 meters
Width ширина | The width in which the mineralization is found in a drill hole Ширина, по которой минерализация находится в буровой скважине | 100 meters
Specific Gravity1 | The density of the ore body (i.e. the rock) | 2.5
Potential mineral deposit value

## Slide 7
As you can see in the example above, the deposit does not have to be enormous in size (only 500 meters long by 100 meters wide) to contain a valuable deposit (approximately $6 billion worth of minerals).
However, in order to be as realistic as possible about this valuation, you can not assume that the complete ore body contains the same grade (i.e. 2% copper and 1.5 gram per ton gold).
In addition, you have to keep in mind that a typical ore body does not fit into a right angled box of three dimensions (strike length, depth and width), as the shape and continuity of the minerals found will be different in every deposit.
Consequently, it is very important to deduct a certain percentage of the calculated mineral deposit value.

## Slide 8: Problem variations
Required Data | 1 | 2 | 3 | 4 | 5 | 6 | 7
Average Grade of copper, % | 1.4 | 1.2 | 1.4 | 1.6 | 2.1 | 1.9 | 2.3
Average Grade of Gold, g/t | 1.2 | 0.9 | 1.1 | 1.3 | 1.2 | 1.15 | 1.4
Strike Length, meters | 480 | 510 | 520 | 515 | 530 | 516 | 518
Depth, meters | 180 | 210 | 200 | 210 | 209 | 215 | 208
Width, meters | 90 | 88 | 94 | 92 | 93 | 95 | 99
Specific Gravity, | 2.08 | 2.25 | 2.30 | 2.09 | 2.42 | 2.5 | 2.46
Problem variations