## Slide 1: Practical lesson #4

## Slide 2
Table 4.1 | Unit Operations in Mineral Dressing |  | 
Process | Description | Properties of mineral exploited | 
Comminution |  |  | 
Crushing, grinding | Subdivision of mineral lumps and particles into smaller sizes | Brittleness | 
Sizing |  |  | 
Sorting or hand-picking, screening | Separation according to size | Size difference among particles | 
Hydraulic classification | Settling in fluid | Relative difference in size and density among mineral particles | 
Concentration |  |  | 
Gravity concentration |  |  | 
Heavy media separa­ tion | Settling in liquid | Relative difference in density among particles | 
Jigging | Settling in liquid | Relative difference in density among particles | 
Tabling | Frictional movement along wet vibrating solid surface | Density, size, shape, and coeffi­cient of friction | 
Magnetic separation | Separation due to magnetic field in dry or wet condition | Magnetic permeability and mag­netic susceptibility of particles | 
Electrostatic separation | Charging and charge loss of particles and their deflections in electrostatic field | Conductivity and charge-retention characteristics | 
Flotation | Attachment of gas bubbles to mineral in aqueous pulp con­ taining surfactants and frothers Subsequent preferential froth flotation for some minerals | Surface properties Affinity for specific surface-active reagents | 
Dewatering |  |  | 
Sedimentation thicken­ing | Settling of particles | Nonspecific | 
Coagulation | Neutralization of charge or re­ pulsive forces | Adsorption properties of minerals may lead to beneficiation | 
Filtration | Solid-liquid separation | Nonspecific | 
Drying | Removal of moisture from moist solid | Nonspecific | 
Agglomeration |  |  | 
Pelletizing, nodulizing, sintering | Obtaining bigger lumps from small particles through adhesion or fusion of particles |  | Solid-solid reaction at s of particles

## Slide 3: Concentration technologies Exercises on Concentration
The objectives of concentration technologies is to separate the valuable mineral from the gangue minerals .In all concentration methods feed is divided in three streams, namely concentrate, middling and tailings.Middlings are recycled within the plant and as such the plant output is two products, namely concentrate and tailings. Tailings are disposed whereas concentrate is sent to metal extraction.
Plants Recovery and grade
Recovery of the mineral in the concentrate and metal grade of the concentrate are important .Recovery is defined as
Grade of the concentrate can be defined either mineral grade or metal grade. Since concentrate is employed for metal extraction, metal grade is important (Note that concentrate contains mineral but not metal).

## Slide 4
Metal grade means grade of valuable metal of the mineral in the concentrate.
For example in the concentrate of chalcopyrite the grade of Сu is important.
Similarly in the concentrate of galena, the grade of Pb is important.
It must be clearly understood that ore does not contain metal. Metal grade is used to give an idea about the removal of gangue minerals and removal of oxygen or Sulphur.
For example mineral grade of pure Fe2O3 is unity but metal grade (or iron grade) of pure mineral Fe2O3 is 70% which means 30% oxygen has to be removed to get iron.
Recovery of a mineral in the concentrate can be 100% if all the feed is diverted in to concentrate. But metal grade will be very low. The maximum metal grade of the concentrate can be that of corresponding pure mineral, for example Cu grade in pure CuFeS is 34.1%, lead grade in pure PbS is 86.6%, Zn grade in pure ZnS is 67%.
Consider 1000 kg feed of chalcopyrite which produces 1000 kg concentrate.
The concentrate contains 500 kg CuFeS 200 kg FeO, 200 kg SiO2 and 100 kg Al2O3 .The analysis of feed is same as that of concentrate.

## Slide 5: Example

## Slide 6: Problem versions
Problem variations
Required Data | 1 | 2 | 3 | 4 | 5 | 6 | 7
Average Grade of copper in feed, % | 0,7 | 0,6 | 0,85 | 0,66 | 0,55 | 0,74 | 0,69
Average Grade of copper in concentrade, % | 29 | 30 | 31 | 32 | 28 | 27 | 26
Average Grade of copper in tailings, % | 0,11 | 0,12 | 0,14 | 0,2 | 0,17 | 0,16 | 0,1
Calculate:
Cu recovery in concentrate
Fraction of feed in concentrate
Enrichment ratio